## Slide 1: Analog to Digital Converters (ADC)
Ben Lester, Mike Steele, Quinn Morrison

## Slide 2: Topics
Introduction
  Why?
  Types and Comparisons
Successive Approximation ADC example
Applications
ADC System in the CML-12C32 Microcontroller

## Slide 3
Analog systems are typically what engineers need to analyze. ADCs are used to turn analog information into digital data.
Notes: a system that can produce many different values.
Voltmeter, thermometer, spedometer

## Slide 4: Process
Sampling, Quantification, Encoding
Output States | Discrete Voltage Ranges (V)
0 | 0.00-1.25
1 | 1.25-2.50
2 | 2.50-3.75
3 | 3.75-5.00
4 | 5.00-6.25
5 | 6.25-7.50
6 | 7.50-8.75
7 | 8.75-10.0
Out-put | Binary Equivalent
0 | 000
1 | 001
2 | 010
3 | 011
4 | 100
5 | 101
6 | 110
7 | 111
Notes: Value of Digital system is taken at determined times, time samples Ts. Use Nyquist Theorem, fs>2*fmax;sampling frequency should be 2 times the max frequency of the analog output.
Quantification: Assigning of input to relative output state. Break up based on number of possible states determined by number of bits for the ADC.
In this example, since there are 8 states, it is a 3 bit ADC.
Encoding is changing the output state to it’s binary equivalent so that it can be used by the computer/circuit.

## Slide 5: Resolution, Accuracy, and Conversion time
Resolution – Number of discrete values it can produce over the range of analog values; Q=R/N
Accuracy – Improved by increasing sampling rate and resolution.
Time – Based on number of steps required in the conversion process.
Notes: Accuracy- higher sampling rate will increase the number of time intervals and resolution will get the output value closer to the analog value.
Speed – varies by type

## Slide 6: Comparing types of ADCs
Flash ADC
Wilkinson ADC
Integrating ADC
Successive Approximation Converter

## Slide 7: Flash ADC
Speed: High
Cost: High
Accuracy: Low
Notes: Image: http://www.acclivities.com/images/clip_image007.gif
Comparator connected to logic switch to encode. Direct conversion ADC.

## Slide 8: Wilkinson ADC
Speed: High
Cost: High
Accuracy: High
Wilkinson Analog Digital Converter (ADC) circuit schematic diagram
Notes: http://fs6.depauw.edu:50080/~akomives/DUNPLweb/summer03/orlayposter.ppt

## Slide 9: Integrating ADC
Speed: Low
Cost: Low
Accuracy: High
Notes: http://www.maxim-ic.com/app-notes/index.mvp/id/1041

## Slide 10: Successive Approximation Converter
Speed: High
Cost: High
Accuracy: High but limited
Notes: “Because the approximations are successive (not simultaneous), the conversion takes one clock-cycle for each bit of resolution desired. The clock frequency must be equal to the sampling frequency multiplied by the number of bits of resolution desired “

## Slide 11: Successive Approximation ADC Example
Mike Steele
Goal: Find digital value Vin
8-bit ADC
Vin = 7.65
Vfull scale = 10

## Slide 12: Successive Approximation ADC Example
MSB  LSB
  Average high/low limits
  Compare to Vin
    Vin > Average  MSB = 1
    Vin < Average  MSB = 0
Bit 7
  (Vfull scale +0)/2 = 5
  7.65 > 5  Bit 7 = 1
  Vfull scale = 10, Vin = 7.65
1 |  |  |  |  |  |  | 

## Slide 13: Successive Approximation ADC Example
MSB  LSB
  Average high/low limits
  Compare to Vin
    Vin > Average  MSB = 1
    Vin < Average  MSB = 0
Bit 6
  (Vfull scale +5)/2 = 7.5
  7.65 > 7.5  Bit 6 = 1
  Vfull scale = 10, Vin = 7.65
1 | 1 |  |  |  |  |  | 

## Slide 14: Successive Approximation ADC Example
MSB  LSB
  Average high/low limits
  Compare to Vin
    Vin > Average  MSB = 1
    Vin < Average  MSB = 0
Bit 5
  (Vfull scale +7.5)/2 = 8.75
  7.65 < 8.75  Bit 5 = 0
  Vfull scale = 10, Vin = 7.65
1 | 1 | 0 |  |  |  |  | 

## Slide 15: Successive Approximation ADC Example
MSB  LSB
  Average high/low limits
  Compare to Vin
    Vin > Average  MSB = 1
    Vin < Average  MSB = 0
Bit 4
  (8.75+7.5)/2 8.125
  7.65 < 8.125  Bit 4 = 0
  Vin = 7.65
1 | 1 | 0 | 0 |  |  |  | 

## Slide 16: Successive Approximation ADC Example
MSB  LSB
  Average high/low limits
  Compare to Vin
    Vin > Average  MSB = 1
    Vin < Average  MSB = 0
Bit 3
  (8.125+7.5)/2 = 7.8125
  7.65 < 7.8125  Bit 3 = 0
  Vin = 7.65
1 | 1 | 0 | 0 | 0 |  |  | 

## Slide 17: Successive Approximation ADC Example
MSB  LSB
  Average high/low limits
  Compare to Vin
    Vin > Average  MSB = 1
    Vin < Average  MSB = 0
Bit 2
  (7.8125+7.5)/2 = 7.65625
  7.65 < 7.65625  Bit 2 = 0
  Vin = 7.65
1 | 1 | 0 | 0 | 0 | 0 |  | 

## Slide 18: Successive Approximation ADC Example
MSB  LSB
  Average high/low limits
  Compare to Vin
    Vin > Average  MSB = 1
    Vin < Average  MSB = 0
Bit 1
  (7.65625+7.5)/2 = 7.578125
  7.65 > 7.578125  Bit 1 = 1
  Vin = 7.65
1 | 1 | 0 | 0 | 0 | 0 | 1 | 

## Slide 19: Successive Approximation ADC Example
MSB  LSB
  Average high/low limits
  Compare to Vin
    Vin > Average  MSB = 1
    Vin < Average  MSB = 0
Bit 0
  (7.65625+7.578125)/2 = 7.6171875
  7.65 > 7.6171875  Bit 0 = 1
  Vin = 7.65
1 | 1 | 0 | 0 | 0 | 0 | 1 | 1

## Slide 20: Successive Approximation ADC Example
110000112 = 19510
8-bits, 28 = 256
Digital Output
  195/256 = 0.76171875
Analog Input
  7.65/10 = 0.765
Resolution
  (Vmax – Vmin)/2n  10/256 = 0.039
1 | 1 | 0 | 0 | 0 | 0 | 1 | 1
Chart: 
| 7.0 | 6.0 | 5.0 | 4.0 | 3.0 | 2.0 | 1.0 | 0.0
volts | 0.5 | 0.75 | 0.875 | 0.8125 | 0.78125 | 0.76563 | 0.75781 | 0.76172
Voltage
Bit
  Vin = 7.65

## Slide 21: ADC Applications
  Measurements / Data Acquisition
  Control Systems
  PLCs (Programmable Logic Controllers)
  Sensor integration (Robotics)
  Cell Phones
  Video Devices
  Audio Devices
t
t
e
e*
Controller
0010
0101
0011
1011
∆t
e*(∆t)
1001
0010
1010
0101
∆t
u*(∆t)